Failure Mode and Effect Analysis (FMEA) for foraging swarm

Robot controller:

EXPLORE	( “un-beaconed” resource found) → BEACON
       |
       |	(beaconed resource found)
      V
COLLECT_RESOURCE → RETURN_NEST → REST → EXPLORE

Hazards investigated:

H1: Avoidance sensor failure
H2:Resource-location sensor failure (a. long-range, and b. short-range)
H3: Nest-location sensor failure (a. long-range, and b. short-range)
H4: Beacon (emitter) failure
H5: Motor failure
H6: Complete robot failure.

Effects considered:

e1: reduction in the number of robots that can perform foraging
e2: reduction in the number of robots that can perform foraging at full efficiency
      [e1 is more serious than e2]

E: drop in rate of foraged resources exceeding 50% (of foraging rate for fully-functioning swarm).

FMEA

H1: Collide into walls and other robots. Other robots may be able to disperse away (not beacon, but such collision will be rare). Effect of hazard will be a reduction in the number of foraging robots (effect e1).

H2a: Damaged robot may take longer to find resources. Small drop in the number of resources collected (effect e2)
H2b: The robot misidentifies the location of the resource, and consequently sets up beacon at the wrong spot. Will result in a large drop in number of foraged resources (effect E).

H3a: Damaged robot may take longer to find nest (effect e2).
H3b: The robot will remain stuck in the RETURN_NEST state (effect e1).

H4: Swarm may take longer to find resources to forage (effect e2 – the beacon is no longer part of the foraging swarm)

H5. Damages robot is stationary (effect e1)

H6: All sub-systems of the robot are shut down (effect e1)
H1: Proximity sensor failure. All 8 IR sensor readings set to 0.
H2: Ground sensor (IR sensors pointing down) failure. All 3 ground sensor readings set to 0.
H3: Light sensor failure. All 8 light sensor readings set to 0.
H4: Range and bearing communication failure. No range and bearing communication information sent or received by damaged robot.
H5: Motor failure.
H6: Complete robot failure.